# Predetermined Pump Pressures

| Required Nozzle Pressures |
| --- |
| Fog Nozzles ( | 100 PSI |
| Low Pressure Fog Nozzle ( | 50 PSI |
| Smooth Bore Hand-line ( | 50 PSI |
| Master Streams ( | 80 PSI |

# Engine Pressure = Required Nozzle Pressure + Friction Loss +/- Elevation

| CAFS (FOAM)( | 110 PSI at the Panel NOT TO BE EXCEEDED |  | APPARATUS COLOR CHART |
| --- | --- | --- | --- |
| 200’ 1”Booster Reel( | 210 PSI at the Panel (60 GPM) w/ Fog |  | 8030 – ORANGE 8051 - BLACK |
| 200’ 1”Booster Reel( | 160 PSI at the Panel (60 GPM) w/ Smooth Bore |  | 8031 – LIGHT GREY 8053 - PURPLE |
| 75’ Bumper Line( | 125 PSI at the Panel (150 GPM) w/Fog |  | 8032 – BROWN 8072 - RED |
| 100’ Bumper Line( | 135 PSI at the Panel (150 GPM) w/Fog |  | 8033 - BLUE |
| 150’ Yellow Pre-connect( | 150 PSI at the Panel (150 GPM) |  | 8035 - YELLOW |
| 200’ Blue Pre-connect( | 170 PSI at the Panel (150 GPM) |  |  |
| 200’ Orange 2” Pre-Connect( | 150 PSI at the Panel (250 GPM) w/ 1 1/8” Smoothbore |  |  |
| 200’ 2 ½” Pre-connect( | 125 PSI at the Panel (250 GPM) |  |  |
| Aerial Master Streams( | 170 PSI at the Base (1000 GPM) |  |  |

|  | Friction Loss in Fire Hose 100’ Lengths |
| --- | --- |
| GPM | 5” | 3” | 2 ½” | 2” | 1-¾” | 1½” | 1” (Booster) |
| 60 | 0 | 0 | 1 | 3 | 6 | 9 | 54 |
| 75 | 0 | 0 | 1 | 5 | 9 | 14 | 84 |
| 95 | 0 | 1 | 2 | 7 | 14 | 22 | 135 |
| 100 | 0 | 1 | 2 | 8 | 16 | 24 | 150 |
| 125 | 0 | 1 | 3 | 13 | 24 | 38 |  |
| 150 | 0 | 2 | 5 | 18 | 35 | 54 |  |
| 175 | 0 | 2 | 6 | 25 | 47 | 74 |  |
| 200 | 0 | 3 | 8 | 32 | 62 | 96 |  |
| 225 | 0 | 4 | 10 | 41 | 78 |  |  |
| 250 | 1 | 5 | 13 | 50 | 97 |  |  |
| 275 | 1 | 6 | 15 | 61 |  |  |  |
| 300 | 1 | 7 | 18 | 72 |  |  |  |
| 325 | 1 | 8 | 21 | 85 |  |  |  |
| 350 | 1 | 10 | 25 | 98 |  |  |  |
| 400 | 1 | 13 | 32 |  |  |  |  |
| 500 | 2 | 20 | 50 |  |  |  |  |
| 600 | 3 | 29 | 72 |  |  |  |  |
| 700 | 4 | 39 | 98 |  |  |  |  |
| 800 | 5 | 51 | 128 |  |  |  |  |
| 900 | 6 | 65 |  |  |  |  |  |
| 1000 | 8 | 80 |  |  |  |
| 1200 | 12 | 115 |  |  |  |
| 1400 | 16 |  |  |  |  |  |  |
| 1500 | 18 |  |  |  |  |  |  |
| 1600 | 20 |  |  |  |  |  |  |

| Master Stream Flow Rates |
| --- |
| Nozzle Tip | GPM |
| 1” ( | 268 |
| 1-1/8” ( | 336 |
| 1-1/4” ( | 415 |
| 1-3/8” ( | 500 |
| 1-1/2” ( | 598 |

| Friction Loss Coefficients |
| --- |
| 1” ( | 150 |
| 1-3/4” ( | 15.5 |
| 2”( | 8 |
| 2 1/2” ( | 2 |
| 3” w/ 2-1/2” couplings ( | 0.8 |
| 3” w/3” couplings ( | 0.68 |
| 5” ( | 0.08 |

| Fire Department Connection Pressures |
| --- |
| Sprinkler Siamese |
| Floors 1-3 ( | 150 PSI |
| Floors 4 and higher ( | 175 PSI plus 5 PSI for each floor |
| Standpipe Siamese |
| Floors 1-3 ( | 165 PSI |
| Floors 4 and higher ( | Add 5 PSI for each floor |
| Appliance Friction Loss: |
| Deck Guns, Wyes and Siamese ( | Add 10 PSI for each |
| Elevation Factors: |
| Below Grade ( | Subtract 5 PSI for each floor |
| Above Grade ( | Add 5 PSI for each floor |

| Hand-Line Nozzle Flow Rates |  |
| --- | --- |
| Nozzle | GPM |  |
| Fog 1-3/4” ( | 150 |  |
| Fog 2-1/2” ( | 350 |  |
| 3/4” Smooth Bore Tip ( | 118 |  |
| 7/8” Smooth Bore Tip ( | 161 |  |
| 1” Smooth Bore Tip ( | 209 |  |
| 1-1/8” Smooth Bore Tip ( | 265 |  |
| 1-1/4” Smooth Bore Tip ( | 328 |  |
| 1-1/2” Smooth Bore Tip ( | 472 |  |
| Cellar Nozzle ( | 100 |  |

| Calculations |
| --- |
| Friction Loss( | Co-efficient X (GPM2 /100) X (Hose Length/100) |
| Engine Pressure ( | Required Nozzle Pressure + Friction Loss +/- Elevation |

| Eductor Calculations |
| --- |
| 95 GPM ( | Eductor Pressure 200 PSI (200’ Maximum lay, 130 Back pressure) Nozzle pressure 100 Psi 1 ¾” hose |
| 60GPM ( | Eductor Pressure 200 PSI (450’ Maximum lay, 130 Back pressure) Nozzle pressure 100 Psi 1 ¾” hose |